## Slide 1: Measurements, maximum errors, % errors, significant figures and decimal places:
Coursework guidance:

## Slide 2: Accuracy
When using a digital measuring device (such as a modern top pan balance or ammeter),
• record all the digits shown.
When using a non-digital device (such as a ruler or a burette),
• record all the figures that are known for certain plus one that is estimated (ending in 5 or 0)

## Slide 3: Maximum errors in measurements:
Half division rule:
4dp Top pan balance: 1.3764g
This has a maximum error of +- half smallest division: 0.00005g but is not estimatible.
Maximum error = 0.0001g
2dp Top pan balance: 1.38g
This has a maximum error of +- half smallest division: 0.005g but is not estimatible
Maximum error = 0.01g
Digital thermometer: 25.1oC
This has a maximum error of +- half smallest division: 0.05oC
Burette is accurate to 0.1cm3
This means it has a maximum error of +- half the smallest division: 0.05cm3

## Slide 4: Maximum errors in measurements:
Glass wear with divisions: Use the grade of the apparatus and the minimum division on that piece of apparatus:
A 100cm3 Measuring cylinder (1cm3 divisions):
Grade A has a maximum error of 0.5cm3
or
Grade B has a maximum error of 1cm3

## Slide 5: Maximum errors in measurements:
Glass wear without divisions: Use the accuracy grade on that piece of apparatus (it is usually written on the apparatus):
Grade B 250cm3 volumetric flask has a maximum error of 0.2cm3
Grade B 25cm3 pipette has a maximum error of 0.06cm3

## Slide 6: % Error:
The maximum error(s) are usually converted to a % error.
This gives you an % error value for your final answer / calculation.
The % error depends on the grade of apparatus used, amounts used and how many decimal places the measuring equipment is accurate to.

## Slide 7: % Error:
This is calculated by:
% error = Maximum error x 100
Quantity used

## Slide 8: % Error:
As an example a 2dp balance has a reading of 2.56g
% error = 0.005 x 100
2.56
% error = 0.2%

## Slide 9: % Error:
Have a go at these:
A 4dp balance = 2.2500g
A 2dp balance = 2.25g
A 2dp balance = 4.50g
A digital thermometer = 34.7oC
A grade A measuring cylinder = 40cm3
A grade A measuring cylinder = 80cm3
A grade B measuring cylinder = 40cm3

## Slide 10: Multiple errors:
For multiple measurements using the same two-decimal place balance, there will be a maximum error of 0.005g for each measurement.
For two mass measurements that give a resultant mass by difference, there are two maximum errors:
Percentage error = 2 × maximum error in each measurement × 100%
quantity measured
For example, using the same two-decimal place balance:
Mass of crucible + crystals before heat = 23.45g maximum error = 0.005g
Mass of crucible + crystals after heat = 23.21g maximum error = 0.005g
Mass lost = 0.23g maximum overall error = 2 x 0.005g
Percentage error in mass loss = 2 × 0.005 × 100%
0.23
= 4.3%

## Slide 11: Multiple errors:
A burette is graduated in divisions every 0.1 cm3. A burette is a non-digital device, so we
record all figures that are known for certain plus one that is estimated.
Using the half-division rule, the estimation is one of 0.05 cm3. We therefore record burette
measurements to two decimal places with the last figure either ‘0’ or ‘5’.
The maximum error in each measurement = 0.05 cm3.
The overall maximum error in any volume measured always comes from two
measurements, so the overall maximum error = 2 x 0.05 cm3 = 0.1 cm3.
In a titration, a burette will typically deliver about 25 cm3 so the percentage error is small.
Percentage error = 2 × 0.05 × 100
25.00
= 0.4%
For small volumes, the percentage error becomes more significant. For delivery of 2.50cm3
percentage error = 2 × 0.05 × 100
2.50
= 4%

## Slide 12: Mean titres
A student obtaining concordant titres within 0.05 cm3 of one
another may encounter a problem:
when calculating the mean titre. For example, a student may obtain
three recorded titres of
25.80cm3 25.25cm3 25.20cm3.
The mean titre is = 25.25 + 25.20
2
= 25.225cm3
This mean titre has a value that is more accurate than the burette can
measure.
The value of 25.225cm3 should more correctly be ‘rounded’ to
25.23cm3.

## Slide 13: Significant figures:
The result of a calculation that involves measured quantities cannot be more certain than the least certain
of the information that is used.
So the result should contain the same number of significant figures as the measurement that has the
smallest number of significant figures.
A common mistake by students is to simply copy down the final answer from the display of a
calculator. This often has far more significant figures than the measurements justify.
Rounding off:
When rounding off a number that has more significant figures than are justified (as above), if the last
figure is between 5 and 9 inclusive round up; if it is between 0 and 4 inclusive round down.
For example, the number 350.99 rounded to:
4 sig fig is 351.0
3 sig fig is 351
2 sig fig is 350
1 sig fig is 400
Notice that when rounding you only look at the one figure beyond the number of figures to which
you are rounding, i.e. to round to three sig fig you only look at the fourth figure.

## Slide 14: Procedural errors:
The accuracy of a final result also depends on the procedure used. For example, in an enthalpy experiment, the measurement of a temperature change may be precise but there may be large heat losses to the surroundings which affect the accuracy of overall result.